## Slide 1
Development of a PHITS simulation technique and a numerical method to optimize measures against radioactive sources
N. Furutachi1, T. Yoshida1, H. Yanagi1, Y. Hasegawa1, and M. Machida2
Research Organization for Information Science and Technology (RIST)
Japan Atomic Energy Agency (JAEA)
We have developed the radiation dose evaluation system for indoor environments:
3D-ADRES-Indoor.
3D-ADRES-Indoor is mainly designed for two applications:
  Estimation of radioactive source distributions with the
  machine learning technique
  Planning of measures against estimated radioactive sources
3D-ADRES-Indoor uses Particle and Heavy Ion Transport code System (PHITS) for the ambient dose rate calculation required for these applications.
Introduction
Estimation of radioactive source distribution
Machine learning – Lasso(and Lasso variants)
G = |Y – AX |2 + λ|X |
Minimize G to determine X
Planning of measures against radioactive sources
In this work,
  A PHITS simulation technique for planning of measures against radioactive sources
  A Numerical method to optimize decontamination rate
have been developed.
PHITS simulation technique for planning of measures against radioactive sources
A technique to reduce calculational cost of simulating four kinds of measures against radioactive sources: decontamination, removal, relocation, and shielding
decontamination
removal
relocation
shielding
Planning of measures against radioactive sources in 3D-ADRES-Indoor
Numerical method to optimize decontamination rate
Estimated high-intensity radioactive source
Observation of ambient dose
Contribution matrix A calculated by PHITS
Removal
Relocation
Decontamination
Shielding
Ambient dose calculated by PHITS
Operations by 3D-ADRES-Indoor GUI
Ambient dose with models incorporating measures is deduced by present PHITS simulation technique
3D-ADRES-Indoor
Example of constructing dose for removal
＝
－
＋
Removal
Base model without removal
Particle Swarm Optimization (PSO) method
Evaluation function
Y : observation vector, X :source vector
A : contribution matrix (dose component at observation point calculated by PHITS)
Dose with models incorporating measures is deduced by following two-step process:
Step 1 – Tally decomposed dose and dump particles impinged on contaminated structure or target region in normal PHITS simulation with base model
Step 2 – Execute simulation using dump source with model incorporating measures and construct dose from equations listed below
Penalty term to suppress dose under target value
Decontamination rates that suppress dose in target region under certain value with minimum cost are obtained by solving constrained optimization problem with penalty term
Conditions of four kinds of measures can be set by 3D-ADRES-Indoor GUI
PHITS input required for present technique is automatically generated
List of structures
Setting of measures
Contaminated structures:
100[Bq/cm2]
Removal
Relocation
Shielding
Step 1: Normal PHITS simulation without measures
Step 2: Dump source simulation and construction of dose with measures
[µSv/h]
Summary
Dose decomposed by PHITS “counter” feature
Radioactive sources widely distributed
Dose without decontamination
[µSv/h]
Suppress dose in target region under 0.1[µSv/h] by decontamination
100[Bq/cm2]
Solve constrained optimization problem by PSO
Import
Dose after decontamination
Under 0.1[µSv/h]
Minimize evaluation function to determine decontamination rates by
Optimized decontamination rate obtained
 | Number of history
Normal simulation | 1000000
Removal × 1 | 6025
Removal × 2 | 12699
Removal × 3 | 14179
Number of history required for dump source simulation of above example
Calculational cost of present technique is notably small compared to normal simulation
The PHITS simulation technique for planning of measures against radioactive sources and the numerical method to optimize decontamination rate have been implemented in 3D-ADRES-Indoor. Users can try more variations of measures with the advantage of the present technique for better planning of measures against radioactive sources. The present work is only a part of various developments around 3D-ADRES-Indoor. Development of 3D-ADRES-Indoor is ongoing.