## Slide 1: My research and topics of interest
Atacan KILICGEDIK
Kandilli Detector, Accelerator and Instrumentation Laboratory (KAHVE-Lab), Turkey
01.11.2024
ISBA24, Chiang Mai University, Thailand

## Slide 2
Kandilli Detector, Accelerator and Instrumentation Laboratory (KAHVELab)- PTAK Project:
1
includes:
*faraday cup (beam current)
*phosphor screen (transverse beam shape)
*pepper-pot (transverse emittance)
MAGNETRON HEAD
*is a passive device with three ports
*serves to protect the power supply from reflected power.
2.45 GHZ CIRCULATOR
MEASUREMENT BOX
MICROWAVE DISCHARGE ION SOURCE
ISBA24, Chiang Mai University, Thailand
20 kEV H+
the applied magnetic field > 875 G

## Slide 3: The 800 MHz RF Transmission Line in the KAHVELab
An solid-state power amplifier capable of up to 5 kW and TH582 tetrode tubes.
Each PSU can deliver up to 35 kW peak power for a typical pulse duration of about 100 µs
ISBA24, Chiang Mai University, Thailand
MAGIC TEE
800 MHZ RF TRANSMISSION LINE
800 MHZ CIRCULATOR

## Slide 4: The PTAK-RFQ at KAHVELab
-HF-RFQ designed in CERN– for use in medical applications,
-PIXE-RFQ designed in CERN– for use in materials science applications
PTAK-RFQ, diameter: 130mm and total length: 980mm
A RFQ has four electrode (called vanes).
The vanes have a longitudinal modulation. This creates a longitudinal component of the electric field. Therefore, not only transverse focusing, but also acceleration of particles can be provided.
PTAK-RFQ utilizes:
*a 3-D special vacuum seal (formed by two circular O-ring and four flat pieces) to obtain the needed vacuum level
*some finger-type RF shields to prevent RF leaks
A photo of the four-vane of the PTAK-RFQ module 0
ISBA24, Chiang Mai University, Thailand

## Slide 5: Bead-pull Measurements for PTAK-RFQ Module 0
For a cavity on resonance, the electric and magnetic stored energies are equal.
If a small perturbation is made on the cavity wall, this will generally produce an unbalance of the electric and magnetic energies, and the resonant frequency will shift to restore the balance.
ISBA24, Chiang Mai University, Thailand
-insert a metallic bead attached to a fishing line into the cavity in small steps along the cavity's longitudinal axis,
-measure the shift in the resonant frequency of the cavity.

## Slide 6: The Field Amplitudes and the Field Tuning Algorithm
The relative quadrant amplitudes of the magnetic field is based on by taking the square root of the smoothed data from each quadrant and assigning proper signs (+, -, +, -) to take into account the alternating field orientation of the TE210 mode denoted as
,
A general arrangement of the magnetic fields obtained by the perturbation measurements in quadrants of the RFQ.
The algorithm gives possible length settings of tuners placed on the module 0 to tune magnetic field distribution.
is the Moore-Penrose pseudo-inverse of matrix R
Singular Value Decomposition (SVD) method is used to decompose . can be factorized as,
R†=VΣ†UT
is obtained by taking the reciprocal of non-zero singular values.
ISBA24, Chiang Mai University, Thailand

## Slide 7: Possible solutions, Field Amplitudes and Final Tuner Positions
The comparison between simulated and measured field components:
Final Tuner Positions:
Before
After
+'s refer to field test points used for the tuning algorithm
ISBA24, Chiang Mai University, Thailand
For each of the 16 possible solutions, there arecorresponding predictions,
R
+