## Slide 1
Optimization of electron gun design for linear acceleration
Rajendra Satriya Utama
Nuclear Engineer – Universitas Gadjah Mada

## Slide 2
Introduction
  BRIN wants to develop a 6 MeV Linac for industrial purpose
  Electron gun performance is crucial for Linac's efficiency
  The design is based on an electron gun for Linac at SLRI, Thailand
  This study focuses on improving beam characteristics through geometric optimization using CST Particle Studio software

## Slide 3
Electron gun design
  Pierce-type electron gun design for 6 MeV Linac
  Thermionic cathode with spherical surface
    Efficient electron emission
    Focused beam generation
  Three-electrode structure
    Pierce electrode with slope and nose
    Focusing electrode
    Anode with nose design

## Slide 4
  Model development
    3D CAD sketching -> CST PS implementation
    Parametric modeling for optimization
  Simulation configuration
    Electrostatic solver:
      30 kV voltage difference (cathode-anode)
      Hexahedral meshing
      Space charge limited emission model
      Electron trajectory analysis
  Optimization & documentation
    Parameter optimization studies
    Engineering drawings (Inventor)
Methodology

## Slide 5
simulation result

## Slide 6
Current | 0,51 | A
Perveance | 9,80E-08 | A/V^(3/2)
Emittance (x) | 9,41E-06 | mm.rad
Emittance (y) | 8,30E-06 | mm.rad
RMS Beam Size | 0,0756 | mm
Diameter Beam | 0,3024 | mm
Results

## Slide 7
Thank You
1-9 Nov 2024 ISBA24