## Slide 1: Electron Injector and Linear Accelerator
Masao KURIKI
Hiroshima University
The 9th International School on Beam Dynamics and Accelerator Technology (ISBA26)
Hosted by Hiroshima University

## Slide 2: Electron Injector and Linear Accelerator
Introduction
Injector
Linear Accelerator
Linear Accelerator
Beam loading and its control
Summary
Summary

## Slide 3: Introduction

## Slide 4: What is Linear Accelerator?
A linear accelerator consists of a particle source, accelerator sections, and an application area.
A linear accelerator is an accelerator that does not have an orbit in the accelerator section.
The accelerator can have an electrostatic accelerator or a radio-frequency accelerator.
Particle source
Accelerator
Application
LINAC
Not
a LINAC
LINAC

## Slide 5: Static and RF LINAC
In an electrostatic linear accelerator, the beam energy is limited by the discharge limit. They are suitable for continuous high-current low energy electron beam.
Beams from radio-frequency linear accelerators are localized bunches in time that are sufficiently shorter than the period of the radio frequency. The repetition of the bunch is at its maximum at the frequency of the accelerating RF. Continuous beam acceleration is impossible, but there is no upper energy limit in principle.
In this lecture, we study the electron RF LINAC.
Continuous beam
Bunched beam

## Slide 6: Components of LINAC
A LINAC is composed from
Electron Gun and Injetor ( Prof. Qian)
RF accelerator (RF cavity by Prof. Fang, SC accelerator by Prof. Zhai)
Beam diagnostic section (Beam Diagnostics by Prof. Leng)
Application area (Collider, FEL, Industrial Application, Medical Application, etc. )
Beam dump

## Slide 7: A typical configuration of Electron Linac
Particle source
Accelerator
Injector
Application
Beam Dump
Electron beam is generated. The temporal structure depends on the technology.
The beam is transformed to a bunched structure for RF acceleration
The bunched beam is boosted by the accelerator section.
The beam is used for various applications.
The beam is dumped with the appropriate radiation shield.

## Slide 8: Electron Gun

## Slide 9: Elements of Electron Gun
Cathode (Electron Emitter)
Extraction Field

## Slide 10: How Much Current ?
Electron current density from a Electron Gun max(,).
  : Highest current density emitted from the cathode.
  :Highest current density limited by Space charge.
We need high brightness cathode and enough electric field for extraction.

## Slide 11: Beam Emittance
Beam emittance is area of the phase-space occupied by the beam particles.
The beam emittance is quality of beam.
The generated beam from a cathode has a value of emittance : Intrinsic emittance.
Thermal cathode
Photo cathode
Small emittance : small area and low equivalent temperature

## Slide 12: Injector

## Slide 13: Role of Injector
The role of injector is preparing “beautiful electron bunches” for acceleration.
What is “the beautiful bunch”?
  Confined in a small region: the bunch is concentrated in a longitudinal small region comparing with the RF period.
  Good synchronization: The bunch repetition is synchronized with RF period.
  No deformation: No correlations among degree of freedom, no non-linear deformation in phase-space of a degree of freedom.

## Slide 14: Good concentration and Synchronization
Bunch length (longitudinal distribution) should be much shorter than RF period for uniform acceleration.
All bunches should be placed on a same phase.
Not beautiful
Beautiful !

## Slide 15: No deformation
No correlation among degree of freedoms, e.g. x and y.
No non-linear deformation in a degree of freedom,e.g. x and x’.
=
w
w’

## Slide 16: What is Wrong?
If there is any correlation between degree of freedoms, or in a degree of freedom, the beam size (or projected emittance) is inflated.
The inflated “emittance” can‘t be recovered by any linear transformation ( quadrupole and drift).
w
w’

## Slide 17: Pre-bunching

## Slide 18: Pre-bunching
Some particle source generates continuous beam.
Any RF accelerator can’t accelerate the continuous beam. It should be transformed into a bunched beam structure.
The repetition of the bunch should be exactly the same as that of the accelerator RF or its sub-harmonics.
The bunched structure is made by an RF cavity whose frequency is the same as the accelerator or its sub-harmonics.
After the pre-bunching, the basic beam structure is formed.
Continuous beam
RF period or its sub-harmonics
Bunched beam

## Slide 19: Velocity modulation and Pre-bunching
The continuous beam passes through the pre-bunch RF cavity.
Particles are accelerated or decelerated depending on the RF phase resulting in a velocity modulation on the beam.
Accelerated particles move forward and decelerated particles move backward after the modulation.
Particles are gathered at the zero-cross of pre-bunching RF with an appropriate drift length.

## Slide 20: Bunching

## Slide 21: Bunch Compression
In RF accelerators, the beam should be concentrated in a short period of longitudinal space for uniform acceleration.
In some case, extremely short bunch length is required.
The bunch compressor (Buncher) shortens the bunch length down to an adequate size.

## Slide 22
There are two ways for bunch compression:
  Velocity Bunching
  Magnetic Bunching
Velocity bunching
  Bunching is performed by the velocity modulation by RF cavity.
  It works only in low energy (low ).
Magnetic bunching
  Bunching is performed in a section with momentum compaction by energy modulation.
  It works for all energy region.
Acceleration
Deceleration
Acceleration
Deceleration

## Slide 23: Velocity Bunching
Bunch compression is performed by velocity modulation within a bunch;
  Bunch head is decelerated.
  Bunch tail is accelerated.
Velocity is modulated by energy modulation according to
Velocity is saturated to at . Then, it works only for low energy particle ().

## Slide 24
Energy modulation by RF cavity,
Time for drift is
With energy modulation,
If , the particles are gathered at the center,
dt
dt
t
dE/E

## Slide 25: Magnetic Bunching
Energy Modulation: RF cavity.
Momentum compaction: different paths for different energy.
The bunch head (tail) travels a longer (shorter) path and the bunch length becomes shorter.
By E.S. Kim

## Slide 26
Bunch compression is performed by energy modulation with a momentum compaction.
  Chicane, Wiggler, Arc, etc.
A path length difference with a momentum compaction, ∆z is
It works for any energy particle.

## Slide 27: Matrix Formalism
Acceleration
Deceleration
Drift
δ(ΔE/E)
z
Bunching can be formalized with transfer matrix in linear approximation.
Energy modulation is made by RF (acc- and deceleration).
Drift space (velocity bunching) or momentum compaction (magnetic bunching) rotates the beam in phase space with 90 deg.

## Slide 28: R-matrices
Beam transfer in longitudinal phase space,
Drift space
,
Momentum Compation
RF Energy modulation
,

## Slide 29
δ(ΔE/E)
z
Transfer of BC section is given as
With bunching condition
Velocity bunching:
Magnetic bunching:
R65
R56

## Slide 30
δ(ΔE/E)
z
R65
R56
When the bunching condition is satisfied,
The position z2 is independent from z1. The bunch center is determined by RF phase (zero cross).
In general, RF signal is a better reference to determine timing. The bunch position is adjusted by the bunching process.

## Slide 31: Energy Compression
Energy compression is a reverse process of the bunch compression as,
The final energy spread is
δ(ΔE/E)
z
R65
R56

## Slide 32: Space charge emittance growth

## Slide 33: Emittance growth by Space Charge
Space charge effect is deformation of the bunch shape in the phase space by Lorentz force.
If the charge density is uniform, the force is linear. In this case, the emittance is still conserved.
If the charge density is not uniform, e.g. Gaussian, the force is non-linear. RMS emittance shows a significant growth.
w
w’

## Slide 34: Slice mismatch
If the bunch intensity is not uniform in longitudinal direction (z), the emittance growth occurred even the density is uniform in x and y.
The emittance growth is due to slice mismatch, where each slice feels different Lorentz force.
A typical example: Bunch center (pink) is more dense than the bunch end (blue).
w
w’

## Slide 35: Emittance growth compensation
Solenoid focusing can fix the emittance growth due to the slice mismatch.
Solenoid focus the slices.
w
w’
w
w’
w
w’
By drifting, the slices rotates clockwise.
The low density slice come to the waist ealier than the high density, so it catches up the high density slice.

## Slide 36: Solenoid focusing
Paraxial Ray Equation
It leads
With the accelerator notation
If the particle is parallel to the axis from the outside of solenoid,
and .
The equation becomes a simple harmonic oscillation as
The focal length is

## Slide 37: Fringe field
The solenoid field is composed from three parts
Entrance fringe field:
Main field :
Exit fringe field :
As the fringe field, induces transverse motion even the particle initially has no transverse momentum.
The entrance and exit fringe fields are anti-sign giving kicks opposite to each other.

## Slide 38: Transfer Matrix of a Solenoid
Fringe field matrixes are
Solenoid main field is

## Slide 39
With a thin lend approximation,
We focus the beam both in x and y simultaneously.
Total transfer matrix of solenoid is
where
, , , and .
L is the total solenoid length.

## Slide 40: Space Charge Compensation
Electric and Magnetic fields by Cylindrical beam
,
Lorentz force
I
Space charge force (Lorentz force by the beam itself) is scaled as .
Space charge is strongly suppress by acceleration.

## Slide 41: Where should we place the first accelerator?
The electron beam in injector (before the first accelerator) should be carefully handled because,
  Lorentz b is still . The bunch length is easily perturbed by velocity modulation, especially, longitudinal space charge effect.
  Lorentz g is still . Space charge is still significant. Slice mismatch is grown.
After the acceleration, the bunch shape is fixed because
  Velocity modulation doesn’t work because .
  Space charge effect is strongly suppressed. Bunch slice re-adjustment cant be performed.
Conclusion
Place the first accelerator where , the bunch length is minimized and the slice is re-aligned.

## Slide 42: Bunch motion synchronization
δ
z
R65
R56
w
w’
Now, put the first accelerator!
Over focused, too late !

## Slide 43
δ
z
w
w’
E-gun
Solenoid
Buncher
Accelerator
δ
z
δ
z
δ
z
δ
z
w
w’
w
w’
w
w’
w
w’
w
w’

## Slide 44: Linear Accelerator

## Slide 45: Beam Transfer
Phase space
Drift space
Focusing Quadrupole
Defocusing Quadrupole
Particle motion is expressed with products of the transfer matrix.

## Slide 46: Phase space and Twiss parameters
Phase space distribution of the bunch is expressed as an ellipse
where or and . As a matrix form,
where and
, , and are Twiss parameters expressing the phase space distribution of the bunch.
F. Plassard

## Slide 47: Phase space Transformation
Transfer of phase space distribution can be expressed as the transformation of Twiss parameters. The beam transport with a matrix as
and should be
Phase ellipse at ,
=1
Phase ellipse at ,
=1

## Slide 48: Adiabatic Damping
If the beam is accelerated, Lorentz is boosted as
The transverse momentum is conserved during the acceleration,
yields =. is expressed as
Transverse velocity and angle become smaller (Adiabatic Damping).

## Slide 49: Transfer Matrix of Acceleration
If we consider the effect of acceleration as a thin lens approximation, the effect is only on and not on . It is expressed as
where
The Twiss parameter is transformed as
The transformation of Twiss parameters are
The emittance is not an invariant in acceleration. To restore the invariance, we introduce normalized emittance as follows
where is Lorentz factor (not a Twiss parameter).

## Slide 50: Beam shape over the linac
The beam emittance is not an invariant during the acceleration.
and are geometrical emittance and normalized emittance. The beam size is
is twiss parameter beta. The beam becomes smaller as it accelerates, as proportional to .

## Slide 51: Building Blocks
Particle transfer in Linear accelerator can be described with 6x6 matrix with
Where is matrix representation of i-th component of Linear accelerator.
Phase space (Twiss parameters) are transformed as
Where

## Slide 52: Beam Loading and its control

## Slide 53: What is Beam Loading?
We consider multi-bunch acceleration. Many bunches are in a RF pulse.
RF Acceleration field is induced by input RF power.
Initial state : The acceleration field is stabilized by balancing the input power and consumption power.
Beam acceleration : Additional power loss by beam acceleration. Acceleration field is decreased.
Decrease in acceleration electric field due to beam acceleration: beam loading.
Temporal variations in the accelerating field due to beam acceleration: transient beam loading.
Pc
Acc field
Pin
Acc field

## Slide 54: Standing Wave and Traveling Wave
Notes: The temporal response to RF input depends on the operating mode (group velocity) of the accelerating cavity.

## Slide 55: SW Cavity Power Balance
Pi
Stored
Matching
Field
Power
Pr
Pc
Pr
Pc
Start with the full reflection.
Power is gradually filled with a time constant.

## Slide 56: Standing Wave Accelerator
Pin
Pr
P0
W0
V0
Power balance
Express in
With admittance

## Slide 57
Admittance of wage guide (definition of coupling )
Matching condition at the coupling window :
wage guide
cavity
The equation is summarized with

## Slide 58
Differential equation of SW accelerator
Solution with
at

## Slide 59: Introduce Beam
Cavity voltage is determined by not only Input power, but also beam current. Beam current is a source to induce cavity voltage.
Beam consume the cavity stored energy as
If the beam current is a delta function on crest,
Power balance is

## Slide 60
Differential equation of SW accelerator with Beam
Solution with
at
Beam start at
Voltage reduction by beam

## Slide 61: Beam Loading Compensation
Since RF and Beam term have the same time constant can be constant by adjusting amplitude and timing.

## Slide 62: Beam Loading By Bunched Beam
Beam current by a single bunch (delta function),
The differential equation (no RF input) is
Integrating on and taking
giving voltage induced by a single bunch

## Slide 63
The differential equation for t>0 is
We solve the equation with
is Heaviside step function. With many bunches and RF input,

## Slide 64: TW Cavity Power Balance
Input
Power flows through cavities with . No reflection.
The power is filled after the filling time ~
Rest of power is extracted and dumped.
Output

## Slide 65: Traveling Wave Linac
  Assume quasi-constant power flow in TW accelerator.
  Expansion with partial derivative

## Slide 66
Expression in field,
shunt impedance
Constant Gradient condition

## Slide 67: Laplace Transformation
In s-domain, differential and integral operation becomes algebraic operation.
Differential
Equation f(t)
Differential
Equation F(s)
Solution
F(s)
Solution
f(t)
Laplace transformation
Inverse
Laplace transformation
Algebra

## Slide 68
Laplace transformation
By integrating with z,
By integrating with z again,

## Slide 69
Input RF E(t) and Beam current,
Giving
In t-domain,

## Slide 72: Amplitude Modulation
Amplitude modulation on E(t) for compensation,

## Slide 73: Two components AM

## Slide 74: Summary
Linear accelerator is a concept of accelerator which doesn’t have an orbit with accelerator section.
The beam is generated and is bunched for RF acceleration.
Slice mismatch by space charge should be fixed by solenoid focusing.
The place of the first accelerator should be synchronized to the bunching and slice adjustment for high performance acceleration.
To accelerate a multi-bunch pulse uniformly, the beam loading should be controlled.