## Slide 1: Foundation of FEL
Takashi Tanaka
RIKEN SPring-8 Center

## Slide 2
Introduction
Coherent radiation
Amplification mechanism in FELs
Classification of FELs
Overview of Single-Pass FELs
Example of FEL Simulations

## Slide 3
Introduction
Coherent radiation
Amplification mechanism in FELs
Classification of FELs
Overview of Single-Pass FELs
Example of FEL Simulations

## Slide 4: Synchrotron Radiation & Laser
Laser
Photon Science
first observed in 1947
radiation by a relativistic electron beam
work as laser-like sources, where conventional lasers are not available
first realized in 1960
fully coherent source by stimulated emission
applicable in spectral regions where reflective mirrors are available
SR

## Slide 5: Wavelengths Available with Lasers
SR has been a good alternative to “X-ray” lasers!
No mirrors -> no practical lasers

## Slide 6: SR Sources
Magnets to deflect the electron beam and generate SR.
Bending Magnet (BM)
Insertion Device (ID)
Undulator
Wiggler

## Slide 7: Comparison with Various Sources
SR provides much higher brilliance, but total power is not that high.
Brilliance of SPring-8 and other conventional sources
What is brilliance?

## Slide 8: What is Brilliance ?
Brilliance specifies the quality of light for observation of microscopic objects.
The brilliance of a light source with a high total power is not necessarily high.
Brilliance(photons/sec/mm2/mrad2/0.1%B.W.)
~
Source Size x Angular Divergence x Band Width
Total Power

## Slide 9: Brilliance of Typical Light Sources
Specs of SPring-8
- E = 8GeV
- I = 100mA
- L = 1500m
100W Bulb
1mW Laser (pointer)
Which brilliance is higher?

## Slide 10: Example of Brilliance Estimation
Item | Bulb | Laser Pointer
Total Power (W) | 100 | 10-3
Angular Div. (mrad2) | 4px106 | 1
Source Size: (mm2) | 102 | 1
Bandwidth: (%) | 100 | 0.01
Brilliance (photons/sec/....) | ~108 | ~1016
Laser is the best light source to observe the microscopic object!

## Slide 11: SR: Highly Brilliant X-ray Source
Any (short) wavelength is available
As a light source:
  Small source size (~ electron beam)
  High directivity
  Quasi monochromatic (undulator SR)
SR works as an alternative to lasers in x-ray regions, however, it is not a laser source at all!
What is different?
Why we need FELs?

## Slide 12: “Coherence” of SR is Poor!
Item | Undulator SR
Temporal | ~10-5 %
Horizontal | ~0.3%
Vertical | ~30%
Total | ~10-8 %
Coherence of typical 3rd gen. SR
(undulator@0.1nm)
Ideally, lasers provide 100% coherent light!

## Slide 13: How FEL Benefits?
Item | Undulator SR | FEL (ideal case)
Temporal | ~10-5 % | ~0.1% (SASE) ~100% (seeded)
Horizontal | ~0.3% | ~100%
Vertical | ~30% | ~100%
Total | ~10-8 % | ~0.1% (SASE) ~100% (seeded)
FEL Peak brilliance is > 1010 higher than SR!
  Even so, SR is still advantageous in some aspects: # users, stability, …

## Slide 14
Introduction
Coherent radiation
Amplification mechanism in FELs
Classification of FELs
Overview of Single-Pass FELs
Example of FEL Simulations

## Slide 15: Spontaneous & Coherent Radiation (1)
In general, 109-1010 electrons are contained in an electron beam (bunch)
Radiation processes are classified according to how photons accumulate
  Spontaneous：random accumulation
  Coherent：in-phase accumulation
Which is more dominant depends on the electron bunch length () relative to the wavelength of radiation (l)

## Slide 16: Spontaneous & Coherent Radiation (2)
l
Spontaneous
Coherent

## Slide 17: Spontaneous & Coherent Radiation (3)
Spontaneous Radiation
  Bunch Length > Wavelength
  Summation as photons: # photons enhanced by N (=# electrons)
Coherent Radiation
  Bunch Length < Wavelength
  Summation as waves: amplitude enhanced by N
  # photons (∝|amplitude|2) by N2
Intensity of coherent radiation is N (=109~1010) times the spontaneous.

## Slide 18: Example of Coherent Radiation
l=30mm
E=8GeV
B=1T
Dt=100fs
Q=100pC

## Slide 19: Coherent Radiation by Microbunches
Coherent at the wavelength of l
FEL is coherent radiation emitted by an electron beam with microbunches
l
Microbunch
l

## Slide 20
Introduction
Coherent radiation
Amplification mechanism in FELs
Classification of FELs
Overview of Single-Pass FELs
Example of FEL Simulations

## Slide 21: Basic Concept of FELs
Electron Beam
Microbunches
Amplified Light
Undulator
Seed Light
What’s the laser medium in FELs?
Free electrons?
Free electrons moving in the undulator field!
z
x

## Slide 22: Electron Trajectory in an Undulator
E=8GeV,K=1,lu=5cm：bxmax=64mrad, xmax=0.5mm
Undulator field with period lu
Transverse
Velocity
Trajectory
K Value
Deflection Parameter

## Slide 23: Velocity Modulations
Original value
transverse velocity
longitudinal velocity
Average Value
Oscillating Term
Undulator magnetic field induces:
  Horizontal (x) oscillation
  Longitudinal (z) oscillation
  Effective deceleration ()

## Slide 24: Keywords to Understand Amplification
The electron trajectory is linked to important 4 keywords in FEL:
  Slippage Effect
  Fundamental Wavelength
  Continuous Interaction
  Longitudinal Dispersion

## Slide 25: Slippage
z
x
: slippage length over lu
= fundamental wavelength l1
e-
photon
Because of the difference in velocity ( and ), photons overtake electrons while they travel along the undulator: Slippage Effect

## Slide 26: Fundamental Wavelength
z
x
Radiation with l1 is in phase with e-
  Intense spontaneous radiation at l1
  Continuous interaction between radiation and e- (next slide)

## Slide 27: Interaction with Radiation
Continuous interaction with radiation
Dg > 0 in (ii), (iv,…)
Dg < 0 in (i), (iii), (v,…)
Periodic energy modulation with l1

## Slide 28: Longitudinal Dispersion
z
x
e-(g)
e-(g’<g)
Higher-energy electrons go ahead of lower-energy ones

## Slide 29: Microbunch Formation in Phase Space
Interaction with Radiation
Longitudinal Dispersion
l1

## Slide 30: Mechanism of Microbunch Formation
Sinusoidal Magnetic Field
Effective Deceleration
Horizontal Oscillation
Energy Modulation
Slippage
Longitudinal Dispersion
Density Modulation
(Microbunch)
Continuous Interaction
Radiation with l1

## Slide 31: FEL Amplification
Microbunching
Coherent Radiation
Coherent Radiation
FEL Amplification =
Positive Feedback Loop of
Microbunching through interaction with radiation
Intensify radiation by coherent radiation
Microbunching

## Slide 32
Introduction
Coherent radiation
Amplification mechanism in FELs
Classification of FELs
Overview of Single-Pass FELs
Example of FEL Simulations

## Slide 33: Classification of FELs
The e- beam moving in the undulator works to “amplify” light
To achieve lasing in FEL, we need
  High gain in total
  Seed light to be amplified
The FELs can be classified according to how to arrange the above conditions
Electron Beam
Microbunches
Amplified Light
Undulator
Seed Light
z
x

## Slide 34: Oscillator FELs
Undulator
Oscillator FEL: original concept
Mirror(Optical Cavity)
Amplified many times by different electrons
Mode selection by the optical cavity
    single mode laser is possible
    challenging in shorter-l (x-ray) regions

## Slide 35: Oscillator FELs
High rep. rate needed (bunch interval = cavity length)
  storage Ring
  multi-bunch linac
Requirement for lasing
  gain/pass > cavity loss
Difficult to be achieved for shorter wavelengths (<100 nm)
  no practical mirrors
Single-Pass FELs

## Slide 36: Single Pass (SP) FELs
Difficulty in oscillator FELs can be overcome by enhancing the gain/pass
  Long undulator
  Higher electron density (lower emittance, higher peak current)
Seed light is amplified by many orders of magnitude even with a single pass
  No cavity is necessary
All of the short-l FELs currently in operation are of this type

## Slide 37
Introduction
Coherent radiation
Amplification mechanism in FELs
Classification of FELs
Overview of Single-Pass FELs
Example of FEL Simulations

## Slide 38: Requirements for “X-ray” SP-FELs
Parameter | Unit | 3rd Gen. SR Facility | X-ray FELs
Emittance | m.rad | 10-8~10-9 | 10-10~10-11
Peak Current | A | 1~100 | 103~104
Energy Spread | % | 0.1 | 0.01
“High Density” e- beam:
not only in 4D (x,y,x’,y’)
but also in 6D (x,y,x’,y’,t,g)

## Slide 39: Generating a High-Density e- Beam (1)
Improvement of emittance and energy spread using Linear Accelerators, instead of Storage Rings
e | ∝ | g-1
sg/g | ∝ | g-1
e | ∝ | g2
sg/g | ∝ | g
LINAC
RING
“the higher, the better”
“the lower, the better” (but more difficult to operate)

## Slide 40: Generating a High-Density e- Beam (2)
Enhancement of the peak current
  “Chirping” and “Compressing”
e- beam
RF Cavity
Lower
Higher
Applying an Energy chirp
t
I
e- beam
Chicane
Bunch Compression

## Slide 41: General Layout of SP FELs
Highly-brilliant Electron Beam
FEL
Pulse
Injector
Bunch
Compressor
Main
Accelerator
Undulator
FEL amplification takes place here!

## Slide 42: Important Parameters in SP-FEL(1)
FEL Parameter r
  Dimensionless parameter related to the efficiency (10-2~10-4)
  FEL bandwidth scales as r
Gain Length Lg
  Undulator length needed to amplify the radiation power by e=2.718
主要パラメータ

## Slide 43: Important Parameters in SP-FEL(2)
slippage in one undulator period
# of periods in one gain length
Cooperation (Coherence) Length lc
  Slippage length in one gain length
  Determines the longitudinal coherence of radiation (spike width) in SASE FELs
主要パラメータ

## Slide 44: Important Parameters in SP-FEL(3)
Saturation Power Psat
  Maximum Power Reached in FEL
Saturation Length Lsat
  Undulator length to reach saturation
Conversion efficiency from e- to radiation is r
Number of undulator periods for saturation is r-1
主要パラメータ

## Slide 45: Type of SP-FELs
Further classified, according to “how to prepare the seed light“
Self-Amplified Spontaneous Emission (SASE)
  Shot noise (spontaneous radiation)
  No limit on l, but poor temporal coherence
Seeded FEL
  External laser light
  High temporal coherence, but shorter-l is challenging

## Slide 46: Shot Noise: Source of SASE
e- distribution contains sparse and dense areas
Radiation profile
temporal
spectral
spatial
angular

## Slide 47: Seeded FEL
Inject “coherent light” synchronously with e- beam
Temporal coherence is significantly improved, if peak power is higher than the shot noise
Two difficulties
  How to guarantee overlapping with the e- beam?
  How to reach shorter wavelength?

## Slide 48: How to Realize Short-l Seeded FEL?
HHG
HGHG
Self Seed
High Power Laser
Dispersive
Section
Monochromator
Undulator
Gas Target
Modulator
Radiator
High Power Laser

## Slide 49: Typical “Gain Curve” in SASE
r
Spont. Rad (SASE)
Exponential Amp.
Saturation

## Slide 50
Introduction
Coherent radiation
Amplification mechanism in FELs
Classification of FELs
Overview of Single-Pass FELs
Example of FEL Simulations

## Slide 51: FEL Simulation
Numerical characterization of radiation is important in many aspects
  deduce the e- beam quality
  design an experiment
Analytical formulas available, but just for a rough estimation
Rigorous simulations needed for quantitative evaluation

## Slide 52: General Method for FEL Simulation
Express the e- bunch by a large number (~106) of macroparticles
  Each macroparticle represents
Undulator is divided into many steps
Within a single step:
  solves the equation of motion for each macroparticle in 6D phase space
  computes the radiation growth by microbunching

## Slide 53: Parameters for Simulation
Electron Beam |  | Undulator | 
Energy | 1 GeV | Period | 50 mm
Bunch Charge | 200 pC | Peak Field | 0.43 T
RMS Bunch Length | 70 fsec | K Value | 2.03
Peak Current | 1.2 kA | Length | 3 m x 10
Norm. Emittance | 1 mm | Source Parameter | 
Energy Spread | 10-4 | FEL Parameter | 2.7x10-3
Average Beta | 10 m | Gain Length | 1.04 m
Beam Size (s) | 70 mm | Wavelength | 20 nm
Angular Div. (s) | 7 mrad | Photon Energy | 62 eV
As an example, results with an FEL simulation code SIMPLEX* are presented in the followings
*T. Tanaka, Journal of Synchrotron Radiation 22, 1319 (2015)
Note: major upgrade in progress

## Slide 54: Gain Curve

## Slide 55: Gain Curve
Spontaneous
Radiation
Exponential
Growth

## Slide 56: Power Enhancement by “Tapering”
Tapering:
dK/dz=-6x10-3

## Slide 57: Temporal Profile
@Segment 1
@Segment 10

## Slide 58: Spike Width vs. Cooperation Length
lc/c=1.4fs
6fs

## Slide 59: Spike Width vs. Cooperation Length
3fs
lc/c=0.7fs
Gain Doubled
1.2kA⇒4.8kA
1 mm⇒0.5mm

## Slide 60: Spectrum
@Segment 1
@Segment 10

## Slide 61: Bandwidth vs. FEL Parameter
rw=0.17eV
0.4eV

## Slide 62: Bandwidth vs. FEL Parameter
rw=0.33eV
Gain Doubled
1.2kA⇒4.8kA
1 mm⇒0.5mm
0.7eV

## Slide 63: Spatial Profile
@Segment 1
@Segment 10

## Slide 64: Angular Profile
@Segment 1
@Segment 10

## Slide 65: Formation of Microbunches
@Segment 7
0.067fs=20nm

## Slide 66: Visualization of Lasing Process
Click here to see animations showing:
  evolution of radiation profiles (temporal, spectral, spatial & angular)
  motion of macroparticles

## Slide 67: Seeding Option
Seeding by coherent light improves the temporal coherence (spectral property)
Coherent light with l=20nm
  Not impossible by HHG, but not so easy (as FEL seeding)
  HGHG (FERMI) scheme is more standard as of now
  Even so, let us assume “20nm/1MW/ 30fs” pulse is available & see how seeding works

## Slide 68: Gain Curve
Seeded
SASE

## Slide 69: Temporal/Spectral Profiles
Seeded
SASE

## Slide 70: Shot-to-Shot Fluctuation
Seeded
SASE

## Slide 71: 10-Shot Average
Seeded
SASE

## Slide 72: Technical Issues
Realization of seeded FELs requires:
  Spatial and temporal synchronization
  Generation of coherent light
FEL performances are more sensitive to the e- beam quality
  Energy chirp is the most critical
Many seeded-FEL schemes proposed
  toward shorter wavelengths
  toward shorter pulse lengths

## Slide 73: Other Topics …
FEL equation: derivation and solution
3D and other effects to evaluate the practical FEL gain
Self seeding for shorter wavelengths
Special schemes for pulse shortening
Polarization property and its control
Details of numerical methods for FEL simulations
…

## Slide 74: Thank you for attention!