## Slide 1
Masao KURIKI
Graduate School of Advanced Sciences of Matter,
Hiroshima University
Super-Flat Beam Generation
with Emittance Exchange Technique for Linear Colliders
16th High Brightness and RF Electron Gun Workshop
ALLPPT.com _ Free PowerPoint Templates, Diagrams and Charts

## Slide 2: Contents
Introduction,
Emittance Exchange,
Super-flat beam generation for linear colliders,
Summary

## Slide 3: Introduction
Emittance is defined as the volume in 6D phase-space.
The 6D emittance is invariant (Loisville's theorem).
2D emittance is not invariant, even with a linear optical element.
That leads that 2D emittances (x, y, z) can are operable.
ｘ
px
z
ｙ
ｘ
px
py
pz

## Slide 4: XY-Z Emittance Exchange TLEX (Transverse to Longitudinal Emittance eXchange)

## Slide 5: TLEX
TLEX can be made with chicane or two doglegs and a dipole mode RF cavity.
The phase spaces of X(transverse direction in deflecting plane) and Z (longitudinal direction) are swapped.

## Slide 6: Transfer Matrices
One dog-leg section
Dispersion
Momentum compaction
Effective length
TM011cavity

## Slide 7: EEX Matrix
matching condition
x-z space exchange
by the 4D space rotation.
compression
factor
dilution
factor
x0
z1
otsuki

## Slide 8: Tunable Subpicosecond Electron-Bunch-Train Generation Using a Transverse-To-Longitudinal Phase-Space Exchange Technique
Y.-E Sun, et al.,
PRL(105)2340801(2010)

## Slide 9
Primary modulation
(slits in x)
After Z-X rotation
(y corresponds to z)
RMS<300fs
(limited by resolution)

## Slide 10
XY Emittance Exchange
RFTB(Round to Flat Beam Transformation)

## Slide 11: Magnetized Beam
Vector Potential
In sigma matrix
Magnetized Beam
Beam Generation in solenoid makes the Canonical angular momentum by Vector potential.
By the fringe field, the canonical momentum becomes the kinetic momentum .
The x-py and y-px correlated beam is obtained.

## Slide 12: Restoration Matrix
E. Thrane, LINAC2002
By ignoring the intrinsic emittance, the beam at the exit of the solenoid field are correlated in x and y.
If the condition is satisfied, Y1 is independent from X0. The correlation is restored.

## Slide 13: How to restore?
Sigma matrix at the downstream of solenoid field has the non-diagonal components.
The non-diagonal component is vanished by M if the correlation is removed by the transfer.

## Slide 14: M matrix
Let us assume three skew Qs
Assume
To satisfy

## Slide 15: Restoration Matrix
E. Thrane, LINAC2002
After skew Q channel,

## Slide 16
P.Piot, Y.-E Sun, K.-J. Kim
PRSTAB(9)031001(2006)
Emittance Ratio 100
was achieved.

## Slide 17: Asymmetric Beam for Linear Collider
Linear Collider is an only solution for e+e- collision beyond the limit of ring colliders due to the huge energy loss by synchrotron radiation.
The beam is “one pass” and the beam current is very limited for linear collider.
To obtain an enough luminosity, the beam is focused down to nm.

## Slide 18: Luminosity Optimization
18
Luminosity
Energy Spread by Beamstrahlung
Large luminosity and suppressed BS is obtained with
Parameter | Value
Horizontal size | 640 nm
Vertical size | 5.7 nm
Bunch length | 300 mm
Vertical Disruption | 19.4
RMS energy by BS | 2.4%
Horizontal emi. | 10 mm.mrad
Vertical emi. | 0.04 mm.mrad
Notes: 18

## Slide 19
The high aspect ratio beam is generated by a 3km DR (Damping Ring) in the current design (ILC TDR).
I the beam can be generated directly from the injector with EmiX technique, the design can be much simpler.
High Aspect Ratio Beam by EMIX

## Slide 20: Emittance Budget
The flat beam for LC (ex=10mm, ey=0.04mm) might be generated with RFBT (xy rotation). In that case, the initial emittance is ex=ey=0.6mm.
In this case, a strong non-linear space charge with 4.8nC bunch charge is concerned.
To solve this issue, RFBT + TLEX are considered.
In this case, the beam is generated in a large spot size and converted to LC compatible beam with a large ez.
 | RFBT |  | RFBT+TLEX | 
 | Initial | End | Initial | End
[Pi mm mrad] | 0.6 | 10 | 50 | 10
[Pi mm mrad] | 0.6 | 0.04 | 50 | 0.04
[Pi mm mrad] | 10 | 10 | 10 | 62500
 | 4 | 4 | 25000 | 25000
 | RFBT |  | RFBT+TLEX | 
 | Initial | End | Initial | End
 | 0.6 | 10 | 50 | 10
 | 0.6 | 0.04 | 50 | 0.04
 | 10 | 10 | 10 | 62500
 | 4 | 4 | 25000 | 25000

## Slide 21: The Beam Line
GaAs/GaAsP
Super-lattice
laser
Polarized Beam
B field
To booster
Skew Quadrupoles
Injector Linac
Dipole Mode
RF cavity
Dogleg
Dogleg

## Slide 22: Beam Test at STF-KEK
STF（Superconducting Test Facility) at KEK
Test facility for Superconducting Accelerator.
L-band RF electron gun
14 L-band Superconducting accelerators.
RFBT+TLEX demonstration
Putting skew Q channel for RFBT demonstration. A solenoid field on cathode can be implemented by inverse the bucking coil polarity.
Implementation and demonstration of TLEX is a future project.

## Slide 23: RFBT Demonstration at STF
Gun
SCL
Q1
Q2
Q3
Q5
Q6
SCL
×12
Q9
Q12
Q13
Q16
×2
skew1
skew2
skew3
SkewQ×3 and Q×2 are newly installed in the existing STF beam line.
Demonstration of an asymmetric emittance beam generation with RFBT and the measurement.
A simulation study was made.
Q17
Q18
OTR
Newly installed
Qscan section
SkewQ channel

## Slide 24: SkewQ channel
RFBT employs 3 skew Q magnets.
Chromaticity of the skew Q is one of the source of emittance growth.
To suppress the chromaticity, amplitude should be low.
Distance of skew Q magnets should be 3 m or more.
skewQ
1
SkewQ
2
SkewQ
3
d2
d3

## Slide 25: Skew Q channel and Qscan section
Q12
Q13
PRM-06
SCR+OTR
3.000m
3.486m
5.394m
BL
1m
1m
0.7m
skew1
skew2
skew3
Q
Q
OTR

## Slide 26: Parameters
Parameter | Value | Unit
Initial emittance εnx,ny | 0.81 | Pi mm mrad
Solenoid field BC | 〜800 | Gauss
Bunch length σz | 3 | ps
Initial Beam size σx,y | 0.8 | mm
Initial beam energy Ekin | 0.75 | eV
Bunch charge | 0.5 | nC
Expected value by linear dynamics (Theory)

## Slide 27: Result (No space charge)
Chart: s[m]
ASTRA+ELEGANT
Theory
※including Chromaticity
Close to that by linear dynamics
sk1
sk2
sk3

## Slide 28: Result (With Space Charge)
ASTRA+ELEGANT
Theory
eny is six times larger.
Space charge in near of cathode is the reason.
Further suppression should be made.
Chart: s[m]

## Slide 29: Larger Beam Spot
e- by tracking is grown comparing to e- by theory.
The reason is not understood yet.
Geometrical aberration ?
Theoretical
Tracking
No space cahrge

## Slide 30: Summary
RFBT and TLEX realize manipulation of among emittances of different axe.
Linear collider requires small emittance beam in x and y with a large asymmetry.
Instead of radiation damping with DR, RFBT and TLEX could make the beam.
Emittance growth with a larger beam size should be understood.
Demonstration of RFBT will be made in STF.
Full demonstration of RFBT + TLEX is possible if we add TLEX at the downstream.

## Slide 31: Robust Spin Polarized Electron Source
p-type GaAs
Fermi
level
Valnece Band
Conduction Band
Thin
film
vacuum
NEA
Φ
EBG
A stable NEA (Negative Electron Affinity) surface on GaAs for a robust spin polarized electron source.
The robust spin polarized electron extend the operability of the beam parameter greatly at the electron source.
According to the hetero-junction model, a stable thin-film on GaAs with a condition make the robust NEA cathode : EBG – f >0.
Candidates are CsTe, CsKTe, etc.
NEA activation (electron emission at EBG photon energy) was observed with CsTe and CsKTe thin films.
Activation with CsKTe : Te 14 Å
EBG~1.4eV
K. Masaki

## Slide 32: Acknowledgement
P. Piot (Northern Illinois University),
J. Power (ANL),
H. Hayano, N. Yamamoto, Y. Seimiya (KEK),
S. Kashiwagi (Tohoku University),
K. Sakaue(U of Tokyo),
M. Wahio (Waseda University),
R. Tamura, T. Nishimura, K. Masaki(Hiroshima U.)
This work is partly supported by Japan-US
Cooperative grant for scientific studies,
Grant aid for scientific study by MEXT Japan (KAKENHI)

## Slide 33: RFBT simulation : Beam size
Chart: Beam size (rms)[mm]
Beam size dependence was studied with ASTRA.
At the larger beam size, the emittance ratio becomes much smaller than that expected with a proper rotation (theoretical).
The coupling emittance is large at the large beam size.
It shows that a more fine adjustment is needed at the large beam size to obtain the high emittance ratio.
Coupling emittance [mm.mrad]
R. Tamura

## Slide 34: RFBT simulation : Solenoid field
Chart: Max B[T]
| 0.126 | 5.0000000000000001E-3 | 0.01 | 1.4999999999999999E-2 | 0.02 | 2.5000000000000001E-2 | 0.03 | 3.5000000000000003E-2 | 0.04 | 4.4999999999999998E-2 | 0.05 | 5.5E-2 | 0.06 | 6.5000000000000002E-2 | 7.0000000000000007E-2 | 7.4999999999999997E-2 | 0.08 | 8.5000000000000006E-2 | 0.09 | 9.5000000000000001E-2 | 0.1 | 0.105 | 0.11 | 0.115 | 0.12 | 0.125 | 0.13 | 0.13500000000000001 | 0.14000000000000001 | 0.14499999999999999 | 0.15 | 0.155 | 0.16 | 0.16500000000000001 | 0.17 | 0.17499999999999999 | 0.18 | 0.185 | 0.19 | 0.19500000000000001 | 0.2 | 0.20499999999999999 | 0.21 | 0.215 | 0.22 | 0.22500000000000001 | 0.23 | 0.23499999999999999 | 0.24 | 0.245
emittance ratio | 772.5733 | 3.6304 | 9.6087 | 19.4534 | 33.3648 | 51.5049 | 74.0149 | 101.0322 | 132.6799 | 168.9919 | 209.9976 | 255.4865 | 305.1108 | 358.1663 | 395.2677 | 470.0498 | 525.6731 | 578.5384 | 626.7892 | 668.7908 | 703.5907 | 688.2311 | 750.4006 | 763.2439 | 770.3249 | 772.5918 | 771.0664 | 766.6993 | 760.2397 | 32.8896 | 743.106 | 733.2127 | 722.6413 | 618.4336 | 700.1701 | 688.3273 | 675.9765 | 663.0675 | 649.7032 | 635.7619 | 621.3244 | 317.0247 | 590.3931 | 575.1408 | 19.917 | 542.6994 | 526.3195 | 249.0583 | 494.0029 | 32.511
Coupling emittance | 0.020809 | 0.014311 | 0.01335 | 0.0012892 | 0.0099752 | 0.012811 | 0.014451 | 0.015713 | 0.0094188 | 0.018332 | 0.019763 | 0.021281 | 0.022799 | 0.024201 | 0.048178 | 0.026278 | 0.026843 | 0.027053 | 0.026791 | 0.02597 | 0.024447 | 0.10116 | 0.018122 | 0.01154 | 0.010163 | 0.019405 | 0.02596 | 0.031464 | 0.018203 | 0.44538 | 0.043572 | 0.045804 | 0.055037 | 0.25488 | 0.043883 | 0.06294 | 0.065376 | 0.047869 | 0.054958 | 0.036857 | 0.032871 | 0.69846 | 0.15176 | 0.024019 | 1.5473 | 0.028373 | 0.033308 | 0.6692 | 0.047215 | 2.6257
Chart: Max B[T]
| 0.126 | 5.0000000000000001E-3 | 0.01 | 1.4999999999999999E-2 | 0.02 | 2.5000000000000001E-2 | 0.03 | 3.5000000000000003E-2 | 0.04 | 4.4999999999999998E-2 | 0.05 | 5.5E-2 | 0.06 | 6.5000000000000002E-2 | 7.0000000000000007E-2 | 7.4999999999999997E-2 | 0.08 | 8.5000000000000006E-2 | 0.09 | 9.5000000000000001E-2 | 0.1 | 0.105 | 0.11 | 0.115 | 0.12 | 0.125 | 0.13 | 0.13500000000000001 | 0.14000000000000001 | 0.14499999999999999 | 0.15 | 0.155 | 0.16 | 0.16500000000000001 | 0.17 | 0.17499999999999999 | 0.18 | 0.185 | 0.19 | 0.19500000000000001 | 0.2 | 0.20499999999999999 | 0.21 | 0.215 | 0.22 | 0.22500000000000001 | 0.23 | 0.23499999999999999 | 0.24 | 0.245
emittance ratio | 229.8405 | 1.0048 | 1.0333 | 1.0155 | 0.95238 | 0.97565 | 0.95594 | 1.081 | 1.1398 | 0.86639 | 1.0087 | 1.0023 | 1.4699 | 1.2662 | 2.7076 | 2.4892 | 7.5655 | 1.1208 | 17.9905 | 23.3294 | 29.6081 | 37.2916 | 48.2619 | 67.8143 | 113.4691 | 214.291 | 181.3761 | 85.677 | 52.6757 | 41.7897 | 38.0712 | 36.7375 | 5.8126 | 1.2912 | 34.2447 | 0.031214 | 17.2662 | 19.3867 | 17.1888 | 15.7106 | 14.7919 | 6.5981 | 6.7827 | 3.9848 | 7.2033 | 7.5587 | 8.0389 | 8.6663 | 9.4452 | 10.4514
Coupling emittance | 0.067242 | 45.6475 | 73483.2686 | 39057.629 | 58674.7912 | 0.17418 | 0.13249 | 0.20634 | 2753.6242 | 42.8211 | 52.3911 | 54.7752 | 1.5341 | 1.9759 | 0.908 | 3.5006 | 0.34622 | 1.1015 | 0.10811 | 0.10863 | 0.10533 | 0.096454 | 0.082117 | 0.056663 | 0.036827 | 0.067428 | 0.018413 | 0.13388 | 0.23672 | 0.30606 | 0.37401 | 0.43759 | 1.7975 | 13.3803 | 1.077 | 0.70754 | 2.8447 | 1.7984 | 1.838 | 1.824 | 1.7821 | 5.4102 | 5.6311 | 12.8195 | 5.6673 | 5.6395 | 5.5624 | 5.4649 | 5.3358 | 5.1977
RFBT simulation (xy emittance exchange) was performed with ELEGANT.
With a proper rotation, the coupling emittance becomes negligibly small.
No space charge: Emittance exchange is successfully done.
With space charge: Emittance exchange is sometimes failed (finite coupling emittance.)
Emittance ratio is saturated at high solenoid field. Need investigation.
No space charge
With space charge
R. Tamura

## Slide 35: Emittance Measurement by Q-scan
εnx=29.59 Pi mm mrad,
εny=0.19 Pi mm mrad
Emittance evaluated from distribution（RMS)
X
Y
Spatial resolution by OTR is not included.
Emittance by Q-scan
（RMS）