## Slide 1: Machine Detector Interface Issues
Mike Sullivan
KEK Accelerator Workshop 2020
January 30-31
KEK, Japan

## Slide 2: Outline
Introduction
Detector Issues
Beam Tails
Machine Issues
Other Issues
Conclusion

## Slide 3: Introduction
KEK
  KEK has continuously pushed the frontier of e+e- colliders
  Tristan was the largest and highest energy collider until the SLC and LEP
  KEKB pioneered crab cavity technology and large angle collisions
  KEKB also set and achieved (x2!) a design goal of 11034 luminosity
    This was a very high number in the early 1990s
SuperKEKB continues this tradition
  Very large angle collision (83 mrad)
  Nano-beam collision
  Lowest by* of any collider (1 mm)
Design parameters
  200 nm by*
  Lumi of 81035
  Beam currents of 2.6 x 3.6 A
    These will be the highest colliding beam currents ever

## Slide 4: Detector Features
Detector acceptance as large as possible
  Usually down to about 15 deg (300 mrad)
Solenoidal magnetic field
  The large crossing angle complicates the beam trajectories in this field
Small radius central beam pipe (1 cm)
  This means that vertex detectors are very close to the beam
The final focus magnets are very close (actually inside) the detector

## Slide 5: Some Detector Issues
Beam Backgrounds
  Coulomb (elastic scattering)
  Beam-gas (inelastic scattering)
  Touschek (inter-bunch scattering)
  Luminosity related
  Beam-beam
  Non-gaussian beam tails
    The beam tail is generated by the above interactions as well as by other effects
    Non-gaussian beam tails can be quite large
    The ee beams have very large damping terms from SR
  Collimation is necessary and crucial in order to control the above backgrounds as well as the SR background from the beam tail
Coulomb
BGB

## Slide 6: More on detector backgrounds
Beam pipe “scrubbing”
  The SR from the electron and positron beams “digs out” the gas molecules imbedded in the beam pipe metal
    This generates gas pressure around the ring “dynamic gas pressure” which can be 10-100 times (or more!) higher than the zero-current base pressure
Synchrotron Radiation is a major background from the beams
  Direct hits on the central beam pipe is the first concern
    These hits are usually coming from beam particles in the high sigma region where there is great uncertainty as to what the actual hit rate will end up being (More on this)
    The direct hit rate generally sets the radius of the central beam pipe
    Direct hits are much more difficult to mask out when the crossing angle is large
  High beam currents force us to worry about secondary scattering
    Forward as well as backward one bounce scattering
    In some cases tertiary (2 bounce photons) can be an issue if the source has a very high incident photon rate
    Usually these rates are not very high and can be ignored but too many hits from a single crossing can swamp a detector by making too much occupancy

## Slide 7: Beam Tails
The core of the beam is assumed gaussian in all 3 dimensions and we believe this is a good approximation
However, any sort of interaction or perturbation of the beam particles can result in a beam particle getting out of this 3D gaussian distribution
For electron (and positron) beams this “out of the envelope” beam particle, in many cases, has an excellent chance of damping back into the core distribution before it hits the dynamic aperture limit of the ring or hits a collimator and is lost
  Synchrotron radiation damping is very strong

## Slide 8: Beam Tails (2)
What this essentially means is that sources of beam particle perturbation or interaction are constantly pushing beam particles out into the high beam sigma region (out into the non-gaussian tail) and SR is constantly pulling (damping) most of these particles back into the core distribution
The result is a semi-stable distribution of beam particles out in the high sigma non-gaussian tail in all 3 dimensions
The larger the dynamic aperture – the more beam sigmas the particle can be in and still stay in the machine
  Machine designs strive to make the dynamic aperture as large as possible

## Slide 9: Beam Tails (3)
Initially, during machine commissioning, the main sources of beam particle interaction are beam-gas collisions (this is the scrubbing phase)
    The luminosity is low, the tune shifts are low, the beam currents are low
  All beam pipes have gas molecules imbedded probably throughout the metal
  Baking out the vacuum chambers gets rid of the surface and near surface gas molecules and is very important (especially for water!)
  But the x-rays from the SR are much more penetrating and these photons will get to molecules that are deeper in the metal and give them the energy they need to migrate to the surface and outgas
  The outgassing rate decreases with time as the gas molecules embedded in the metal are gradually removed
  Remember that this applies to the entire inner beam pipe surface
  The strike surface of the SR beam cleans up fairly quickly but the scattered x-rays from the strike point must also clean up the rest of the beam pipe inner surface

## Slide 10: Some Non-gaussian Beam Tail Distributions
Suggested early KEK beam tail
Suggested early KEK beam tail
Possible later beam tail
Possible later beam tail
Gaussian
Gaussian
The larger beam tail distribution has about 3.5% of the total particles of the bunch

## Slide 11: Beam Tails (4)
As the initial outgassing diminishes and the beam lifetime increases the accelerator team can start raising the beam currents
  This, of course, increases the outgassing again and a balance must be struck to keep the backgrounds at an acceptable level for data taking
  As the currents increase so do the other beam particle perturbation terms
    The luminosity contribution increases as the lumi goes up (this one we want!!)
    The Touschek lifetime can drop – increasing the background from this source
    Beam-beam effects become important
    Even beamstrahlung can become important
As the machine performance improves the initial sources of non-gaussian particles diminishes but new sources become larger and more important
So, there is always a non-gaussian beam tail distribution in the machine
    Especially in high current rings

## Slide 12: Accelerator Issues
High beam currents
  2.6 A for the 7 GeV electron beam
  3.6 A for the 4 GeV positron beam
Short beam bunches
  ~6 mm
    HOM power around the ring
Feedback systems
  Bunch-by-bunch orbit stability
    Transverse
    Longitudinal
  Luminosity
    Maintain the beams in collision with feedbacks
    Fast enough to compensate for final focus mechanical motion?

## Slide 13: More Accelerator Issues
Clean injection
  Minimize detector background
  Maximize efficiency in order to keep up with short beam lifetimes
Beam emittance
  Minimize orbit deviations in quadrupoles
  Control the dispersion functions
Control the coupling
  Controls the vertical spot size
Control beam size
  Beam blowup
    One beam blowing up the other beam
    Both beams blowing up from the collision
Tunes
  Tune footprint

## Slide 14
PEP-II HER tune plane
PEP-II LER tune plane

## Slide 15: More on accelerator issues
Luminosity
  Low y*
  The accelerator team may discover they can go to lower y* or x* values. Then the y or x max is larger in the FF quads making more SR at larger distances from the beam axis in the FF quads.
Continuous injection
  Low backgrounds
  Collimators can help here but clipping off too much injected beam can harm injection efficiency

## Slide 16: Closely spaced beam bunches
When the bunch spacing gets close (~10 ns) the bunches can start to affect each other
  This is one of the main reasons the beam pipe must have smooth, gentle geometry transitions
    The PEP-II B-factory generally had a limit of 15 deg (1:12) for beam pipe transitions
  The “left behind” RF power can interact with the next bunch
  This bunch to bunch coupling must be controlled by feedback systems
  Smooth transitions minimize this impedance effect
S. Novokhatski has much better pictures of this effect

## Slide 17: Some Conclusions
The accelerator and detector teams need to work closely together to maximize the efficiency of the commissioning phase
  The detector team wants to start taking data as soon as possible
  The accelerator team wants to move to the design machine as quickly as possible
These goals sometimes need a bit of give and take
  Both teams eventually want the same thing – high luminosity and data taking at the same time
The beam tail distributions will change as the machine becomes better understood, as the scrubbing continues, and as the accelerator approaches the design parameters
  However, there will always be some form of non-gaussian tail distribution

## Slide 18: Summary
These are exciting times!
The SuperKEKB accelerator is truly a frontier machine
Many features of this machine need to be better understood
  No one has such a machine to explore this part of accelerator parameter space
What is discovered here will be used in all future collider designs