## Slide 1: ILCにおける中性子発生 Neutron production with ILC
Kenji MISHIMA
KEK, J-PARC
kenji.mishima@kek.jp
ＩＬＣの多角的活用を考える会II
2018/Jul/6th, 京都大学宇治キャンパス

## Slide 2: Contents
Neutron production reactions
Neutron production at ILC
Applications

## Slide 3: Neutron production reactions

## Slide 4: Neutron production reactions
Nuclear reaction
  9Be + 𝛼 → n + 12C
  7Li + p → n + 7Be
  9Be + 𝛾→ n + 8Be
Fission
  235U + n → Fission Products + 2.4 n
Fusion
  D + T → n + 4He En = 14.1 MeV
  D + D → n + 3He En = 2.5 MeV
Spallation
  Hg + p(~GeV) → Fission Products + ~20 n

## Slide 5: Photo Nuclear Reactions
Two candidates for photo nuclear reactions:
  Light and Heavy nuclei
9Be + 𝛾→ n + 8Be (Sn = 1.665 MeV)
D + 𝛾→ n + p (Sn = 2.225 MeV)
  Pros: Low Sn , No structure(monochromatic neutron), small photo attenuation
  Cons: Small cross section
Heavy Nuclei (208Pb Sn= 7.368 MeV etc.)
  Pros: Large Cross section
  Cons: Nuclear structure makes broader neutrons, Large photo attenuation (large energy deposit)

## Slide 6: Photo Nuclear Reactions 9Be(,n)4He
(,n) is 1.2 mbarn at 1690 keV (En=25 keV)
C.W.Arnold et al., PhysRevC.85.044605
9Be(,n)4He cross section
Threshold = 1665.3 keV
Due to detailed balance,
the cross section near the
threshold is expected to be

## Slide 7: Photo Nuclear Reactions 208Pb (,n)207Pb
  40 mbarn at 7.500 MeV
  (En=130 keV)
  at pigmy dipole resonance (PDR)
T. Kondo et al., PHYSICAL REVIEW C 86, 014316 (2012)
(,n) is
  600 mbarn at 13 MeV
  (En=5.6 MeV)
  at giant dipole resonance (GPR)
“Atlas of Giant Dipole Resonances”
(1999) INDC(NDS)-394 Distr. GN+NM
208Pb(,n) 207Pb
Threshold (208Pb) = 7368 keV
GDR peak
PDR resonance
n
p

## Slide 8: Estimation of neutron production 9Be with 1.690 MeV gamma
Cf. 50 MeV / neutron for spallation reaction
Parameter | Value
Target | 9Be
Threshold | 1.66531 MeV
Gamma energy | 1.690 MeV
Neutron energy | 25 keV
Number density | 0.124 atoms/barn/cm
9Be(,n)8Be cross section | 1.2 mbarn
Photo attenuation length | 33 cm
Gamma to neutron conversion rate | 0.61%
Energy input per neutron | 280 MeV

## Slide 9: Estimation of neutron production 208Pb with 13 MeV gamma
Parameter | Value
Target | 208Pb
Threshold | 7.368 MeV
Gamma energy | 13 MeV
Neutron energy | 5.6 MeV
Number density | 0.033 atoms/barn/cm
208Pb(,n)207Pb cross section | 600 mbarn
Photo attenuation length | 1.6 cm
Gamma to neutron conversion rate | 3.2%
Energy input per neutron | 410 MeV
Cf. 50 MeV/neutron for spallation reaction.

## Slide 10: Estimation of neutron production 208Pb with 7.5 MeV gamma
Parameter | Value
Target | 208Pb
Threshold | 7.368 MeV
Gamma energy | 7.5 MeV
Neutron energy | 132 keV
Number density | 0.033 atoms/barn/cm
208Pb(,n)207Pb cross section | 40 mbarn
Photo attenuation length | 1.9 cm
Gamma to neutron conversion rate | 0.25%
Energy input per neutron | 3000 MeV
Cf. 50 MeV/neutron for spallation reaction.

## Slide 11: Neutrons source using Neutron halo isomers in stable nuclei
Habs, D., et al. "Neutron halo isomers in stable nuclei and their possible application for the production of low energy, pulsed, polarized neutron beams of high intensity and high brilliance." Applied Physics B 103.2 (2011): 485-499.
Neutron production by laser/X-ray by neutron halo isomer exited by ICS gamma was proposed by Habs et al. If we can find such a good nuclei, very intense eV-neutrons can be obtained.

## Slide 12: Summary of photo neutron reactions
Photo neutron reactions
  Cross sections are 1 to 600 mbarn.
  Production rate is order of 1%.
  Energy per neutron production is ~300 MeV, which is 6 times larger than spallation reaction (50 MeV).
From the point of view of engineering, the heat removal of the target is very important.
  Ex. J-PARC spallation neutron source
    3GeVx333uA=1MW
    Total neutron production is ~1017/s

## Slide 13: Neutron production at ILC

## Slide 14: Distribution of the Beam Dumps
Most practical use of extracted beam is the ones at the location of the beam dumps (Otherwise, extraction system must be added, which occupies a longitudinal length. Must be planned early.
Distribution of the Beam Dumps is shown below
blue: electron, red: positron
The numbers shown are the upper limit of the beam power to be dumped (20% margin included)
  Mostly for commissioning or emergency except E-5, E+5, E+7, E-8
  Hence the power of the full beam power at the beam line nearby is more than the number here
  The full beam can be dumped only at E-5, E+5, E+7 (The upper limit of the dumps exceeds the full power because future upgrades are taken into account)
E-8 will not be built in ILC250GeV
Yellow arrows indicate the bunch compressors. The rms bunch length is 6mm in the upstream (from DR) and 0.3mm in the downstream.
Bunch Compression
Bunch Compression
E+7
E-4
This slide is from K. Yokoya.

## Slide 15: Beam Dump Specification
PB max = The maximum beam power at the nearby beamline for ILC250GeV
W = Upper limit of beam dump power (20% margin included)
This slide is from K. Yokoya.

## Slide 16: [E+7]
Photons from the undulators to produce positron
  This is absent if the e-driven scheme is chosen for positron production
No variety in the operation mode in case of ILC250GeV
  Electron energy 125GeV (more precisely, 128GeV at undulater section entrance and 125GeV at exit)
  Average energy of all photons 6.3 MeV
  Number of photons generated (about 400 photons from each electron) per bunch 8 x 1012 per second 5.2 x 1016
  Average energy of photons reaching the target 9.7 MeV (Low energy part is eliminated at the masks/collimators)
  Photon power at the target ~ 50 kW
The target is thin (0.2X0). Most photons go through the target and reach the photon dump

## Slide 17: Photon Energy Distribution on Target
x
black: no mask
red: with masks
blue: with masks & collimator (r=2.2mm)
This slide is from K. Yokoya.
9Be/D
208Pb

## Slide 18: Neutron production at E+7 undulator
Parameter | Value
Photon luminosity | 
Photon flux | 
Photon intensity | 5.2 x 1016 photon/s
Total Energy of photon | 50 kW
Target | 208Pb
Gamma energy | 7.5 MeV
Neutron energy | 130 keV
Gamma to neutron conversion rate | 0.25%
Total neutron production | 1 x 1014 neutron/sec
1/1000 of J-PARC

## Slide 19: Neutron production at E+7 undulator
Parameter | Value
Photon luminosity | 
Photon flux | 
Photon intensity | 5.2 x 1016 photon/s
Total Energy of photon | 50 kW
Target | 9Be
Gamma energy | 1.670-1.690 MeV
Neutron energy | 5-25 keV
Gamma to neutron conversion rate | 0.6%
Total neutron production | 3 x 1014 neutron/sec
1/300 of J-PARC

## Slide 20: [E-4, E+4]
Right after ML (main linacs)
Energy 125 GeV
emittance 5mm.rad x 35 nm.rad
Energy spread 0.19% (e-), 0.15% (e+)
  Energy spread of e- is larger because of the radiation in undulator
Bunch length 0.3mm
  As at E+-6, Must be fixed to 0.3mm during collision experiments, but the the bunch compressor itself is capable of compressing the bunch down to at least 0.15mm. (But the energy spread would be doubled.)
  Therefore, if 0.15mm is absolutely needed, it might be possible to borrow a machine time hours/days
Full beam power 2.5MW, beam dump < 400kW
In case of `stealing’ ~10% the reinforcement of beam dump is not needed
Note: The beam parameters at [E-7] are similar to above but the maximum power for this dump is limited to 60kW (because [E-7] is an emergency dump to protect the undulators) . Therefore, the use of [E-7] is presumably less useful than at [E-4, E+4]
This slide is from K. Yokoya.

## Slide 21
Possibility of neutron source using photon beam from ILC
Undulator parameters
Undulator period l : 6.5 cm
Undulator strength K : 0.61
Undulator type: helical
Active undulator length: 20 m
Field on-axis: 0.1 T
ILC main linac parameters @ E-4
Normalized emittance ge : 5.0 x 10-6 m·rad
Total emittance at 125 GeV: 2.0 x 10-11 m·rad
Beam current: 0.58 mA (10% of main current)
Partial Flux thr 25 urad aperture
Peak Photon Energy = 1.66 MeV
This slide is from S.Sasaki.

## Slide 22: Neutron production at E-4 undulator
Parameter | Value
Photon luminosity | 1.5 x 1013 photon/25urad/0.1%B.W/s
Photon flux | 
Photon intensity | 1.5 x 1014 photon/s (5-25 keV)
Total Energy of photon | 40 W
Target | 9Be
Gamma energy | 1.670-1.690 MeV
Neutron energy | 5-25 keV
Gamma to neutron conversion rate | 0.6%
Total neutron production | 1x1012 neutron/sec
10-6 of J-PARC

## Slide 23: Summary of neutron production at ILC
E+7 and E-4 is candidates.
  5x1016 photon/s (50 kW) at E+7 undulator in 100% B.W.
  1014 photon/s at (40 W) at E-4 undulator in 1%B.W.-25 urad
Because the neutron production rate is ~0.3-0.6%, neutron production rate is 1012-1014 neutron/s.
Velocity of 30 keV neutron is 2.4x106 m/s.
If we use bunch structure of 552 ns, TOF length should be less than 1.2 m.

## Slide 24: Applications

## Slide 25: J-PARC Neutron/Muon Lab. (MLF)
Neutron target station
60 m
150 m
1-MW Hg spallation target for neutron source.
Because of pulse structure, ILC neutron facility will be MUCH smaller.

## Slide 26: Application of keV/MeV neutrons
Neutron cross section measurement with high energy resolution by transmission.
  n_TOF@CERN, ANNRI@JPARC, Los Alamos.
Neutron source
~100 m
keV neutron detector
1m
1 m
Resolution of n_TOF@cern
C. Guerrero et al., Eur. Phys. J. A (2013) 49: 27
100 m keV neutron source is possible to measure total cross section with resolution of 10-4, which is better than n_TOF@CERN.
sample

## Slide 27: Application of keV/MeV neutrons Neutron microscopic imaging
Neutron source
~100 m
keV/MeV neutron detector
Sample
1m
1 m
1 mm
1 mm
Neutron imaging with keV/MeV neutrons.
  1000 times larger image can be obtained at sample potions at 1 mm.

## Slide 28: Neutron moderation
低エネルギーのほうが有利だが2~3倍程度
最適化すればもっと効率は上がるか？
2 barn@2MeV
20 barn@20 keV
とある小型中性子源モデレーターの計算

## Slide 29: Summary
Photo-neutron reaction rate was calculated.
  For 9Be(g,n) at 1.690 MeV
  Gamma to neutron conversion rate ~ 0.6%
  Energy input per neutron ~ 280 MeV/n
  Cf. ~ 50 MeV/n for spallation neutron (J-PARC)
5x1016 𝛾/sec produces 1014 n/sec of keV neutrons.
  1,000 times less production than J-PARC
  Heat on the target (50 kW) is the problem.
Application
  keV neutron with TOF
  Thermal neutron with compact moderation
  Direct eV neutron production