## Slide 1: ILC Beam for Outside Users Version 3
K. Yokoya, KEK
2018.7.5 Kyoto Meeting

## Slide 2
Beam parameters of 250GeV ILC for possible users from outside
  Number of bunches per pulse is 1312
  Do not consider the possible energy upgrade (far future)
  There is a possibility to double the number of bunches later. But it requires reinforcement of RF system and cost several 100M$. This possibility is not considered here.
  Pulse repetition rate is 5Hz in normal operation. The rate can be increased up to 10Hz with an investment less than to double the bunches. But it is still uncertain if the positron target can survive under higher repetition rate. So, fix at 5Hz.
  Positron beam is assumed to be produced by the undulator scheme. Electron-driven scheme might be adopted, depending on the situation.
Main concern in this report is the parasitic mode use under Higgs experiments.

## Slide 3: Fundamental Parameters
Pulse repetition rate 5 Hz
Damping Rings
  Beam energy 5 GeV
  Circumference 3238.7 m
  Stored bunches 1312
  Bunch interval 6.15 ns (There are several gaps between trains)
  Number of e+/e- in a bunch 2x1010
  Equilibrium bunch length (rms) 6 mm
  Equilibrium energy spread (rms) 0.11%
  Equilibrium emittance (normalized)
    horizontal 4.0 mm.rad (less than in TDR)
    vertical 20 nm.rad
Interaction Point
  Beam energy 125 GeV
  Number of bunches per pulse 1312
  Bunch interval 554 ns
  Pulse length 0.73 ms
  Bunch length (rms) 0.3 mm
  RMS energy spread (e-/e+) 0.19/0.15 %
  Emittance before collision (normalized)
    horizontal 5.0 mm.rad (less than in TDR)
    vertical 35 nm.rad

## Slide 4: Parasitic Mode Use
Destructive use of a part of the beam (extraction)
  part of the 1312 bunches (head or tail)
    Requires high speed kicker (rise/fall < 0.5ms)
  part of 5Hz pulse (rise/fall < 200ms) (The Japanese version 1 contained a mistake here. Eliminated)
Non-destructive use of a whole or part of the beam
  e.g., insert an undulator in the beam line
  In case of straight section it is necessary to insert a chicane to separate photons and electrons
  Must not degrade the emittance of the main beam
Other possible uses with no influence to the collision experiment
  Use if the beam after collision
  Use of the photons from the undulators for positron production
  Operate the electron injector (5GeV) at 10Hz. Use 5Hz for the parasitic experiment (need to reinforce the power supply, but not expensive)

## Slide 5: Distribution of the Beam Dumps
Most practical use of extracted beam is the ones at the location of the beam dumps (Otherwise, extraction system must be added, which occupies a longitudinal length. Must be planned early.
Distribution of the Beam Dumps is shown below
blue: electron, red: positron
Yellow arrows indicate the bunch compressors. The rms bunch length is 6mm in the upstream (from DR) and 0.3mm in the downstream.
The numbers shown are the upper limit of the beam power to be dumped (20% margin included)
  Mostly for commissioning or emergency except E-5, E+5, E+7, E-8
  Hence the power of the full beam power at the beam line nearby is more than the number here
  The full beam can be dumped only at E-5, E+5, E+7 (The upper limit of the dumps exceeds the full power because future upgrades are taken into account)
E-8 will not be built in ILC250GeV
Bunch Compression
Bunch Compression

## Slide 6: Beam Dump Specification
PB max = The maximum beam power at the nearby beamline for ILC250GeV
W = Upper limit of beam dump power (20% margin included)
  PBmax > W : full-beam cannot be dumped
  PBmax < W : The dump system can accept upgraded beam

## Slide 7: [E-1]
Use of 5GeV electron injector
It is presumably possible to operate the injector at 10Hz, using 5Hz for collider and 5Hz for parasitic experiment
  No problem in klystron 10Hz operation (Euro-XFEL)
  Electron gun (polarized) is perhaps OK (must be confirmed)
  Marx modulator
  Must reinforce the AC power supply
  No influence on the collision experiments
  Beam dump E-1 must be upgraded (to 120kW?)
  Some tunnel extension needed for the experiment.
The beam properties
  Up to version 2 it was said “similar to those in Euro-XFEL except the beam energy”. Here was a big mistake.
  Euro-XFEL adopts RF gun but ILC adopts DC gun for polarization. The bunch length is much longer thab at XFEL. For FEL oscillation it is presumably needed to install RF gun in parallel.
  The electron beam is polarized. Maybe useless?
Note: [E+1] (positron right after production) is presumably useless because of its bad quality

## Slide 8: [E-2,E-3,E+2,E+3]
Exit from Damping Ring [E-2,E+2] and just before bunch compression [E-3,E+3]
5GeV, low emittance (~4mm.rad x 20nm.rad)
But long bunch （6mm）
Same pulse structure as in ML. Bunch separation 554ns, 1312 bunches, 5Hz
Energy spread ~0.11%
Average current is low（~20mA)

## Slide 9: [E-6, E+6]
Just after bunch compression
15GeV, low emittance (~4mm.rad x 20nm.rad)
Energy spread is a bit large ~1.2%
Short bunch （0.3mm）
  Must be fixed to 0.3mm during collision experiments, but the bunch compressor itself is capable of compressing the bunch down to at least 0.15mm. (But the energy spread would be doubled.)
  Therefore, if 0.15mm is absolutely needed for the parasitic experiment, it might be possible to borrow a machine time hours/days, though this is not a parasitic operation.
Full beam power ~300kW, Dump < 60kW
In case of `stealing’ ~10%, the reinforcement of beam dumps E-6, E+6 is not needed

## Slide 10: [E-4, E+4]
Right after ML (main linacs)
Energy 125 GeV
emittance 5mm.rad x 35 nm.rad
Energy spread 0.19% (e-), 0.15% (e+)
  Energy spread of e- is larger because of the radiation in undulator
Bunch length 0.3mm
  As at E+-6, Must be fixed to 0.3mm during collision experiments, but the the bunch compressor itself is capable of compressing the bunch down to at least 0.15mm. (But the energy spread would be doubled.)
  Therefore, if 0.15mm is absolutely needed, it might be possible to borrow a machine time hours/days, though this is not a parasitic operation.
Full beam power 2.5MW, beam dump < 400kW
In case of `stealing’ ~10% the reinforcement of beam dump is not needed
Note: The beam parameters at [E-7] are similar to above but the maximum power for this dump is limited to 60kW (because [E-7] is an emergency dump to protect the undulators) . Therefore, the use of [E-7] is presumably less useful than at [E-4, E+4]

## Slide 11: [E-5, E+5]
Main beam dump. Inside a big dump hall.
Energy 125 GeV
In case of parasitic mode, the beam quality is poor because of the beam collision
  Especially the energy spread is large (several percent) with long low-energy tail
  An example of the electron energy spectrum after collision is shown in the next page
Main dump is located at 300m from the interaction point (IP) in TDR. Since the crossing angle is 14mrad, the beam going to the IP is separated horizontally by 300m x 14mrad = 4.2m. May make `300m’ a bit larger.
Caution
  The beam can be destroyed. But the beam is extremely strong. Quite risky. Looks almost impossible?
  Photons from beamstrahlung come together. Their number is about twice of electrons, the power is 2.6% of electron, average energy 1.7GeV. The energy spread is very large.

## Slide 12: Example of electron energy spectrum after collision

## Slide 13: [E+7]
Photons from the undulators to produce positron
  This is absent if the e-driven scheme is chosen for positron production
No variety in the operation mode in case of ILC250GeV
  Electron energy 125GeV (more precisely, 128GeV at undulater section entrance and 125GeV at exit)
  Average energy of all photons 6.3 MeV
  Number of photons generated (about 400 photons from each electron) per bunch 8 x 1012 per second 5.2 x 1016
  Average energy of photons reaching the target 9.7 MeV (Low energy part is eliminated at the masks/collimators)
  Photon power at the target ~ 50 kW
The target is thin (0.2X0). Most photons go through the target and reach the photon dump

## Slide 14: Photon Energy Distribution on Target
black: no mask
red: with masks
blue: with masks & collimator (r=2.2mm)

## Slide 15: Photon (x-y) Distribution on Target
With masks
See slightly larger horizontal size due to horizontal emittance (horizontal betatron oscillation in the undulator section)
Only randomly selected particles are plotted here
Total number of macro particles is ~400k

## Slide 16: Photon Data
Photon data are stored in
  http://lcdev.kek.jp/~yokoya/temp/BeamOnTarget2017-0526.txt (survived photons on the target. no collimator. Contains some 400k photons)
  http://lcdev.kek.jp/~yokoya/temp/LostPhotons2017-0531.txt (lost photons. Lost position preserved, Contains some 80k photons)
These photons are measured just before the target. The shower developed in the target (thickness 0.2X0) are not included.
Format (macro-particle data from 1 electron bunch)
  1st line: title
  Then (I2, 11X, 12E20.12)
  I2: 1 for photon, 2 for electron
  12E20: w, ct, x, y, s, E, px, py, ps, x1, x2, x3,
  w: 1 macro-particle represents w real particles
  ct : delay time with respect to the bunch center (meter)
  x, y: transverse coordinate at the target (meter)
  s: longitudinal position (same value for all photons = target position)
  E, px, py, ps : enery-momentum (eV, eV/c)
  x: Stokes parameters ( x2= circular polarization)

## Slide 17: Location of the Photon Dump
300kW is assumed with future beam upgrade in mind, but the actual power in ILC250GeV is 60kW at maximum
TDR adopted a dump with high-pressure water and titanium alloy window placed at several 10s’ of meters from the target. But later it turned out this window does not work due to the radiation degradation.
Most probable candidates of the dump is located at 1-2km downstream from the target
In this case the photons will fly through a pipe in the tunnel for the BDS (beam delivery system --- long beam line to focus the beam). 2 beam lines (positron line and BDS line) go in parallel on either side of the photon pipe with distance ~1.5m.
This defines a limit on the size of the devices for the parasitic experim
The most important is the safety in intercepting the strong photon beam for the parasitic experiment.
photon dump
target
capture section
BDS
target
capture section
photon dump
BDS

## Slide 18: Use of the Beam in Damping Rings
Space for insertion devices are not reserved at present
Beam current ~0.5A
The equilibrium emittance is small. However, it takes time to reach the equilibrium and the beam is extracted immediately after equilibrium is reached.
Therefore, the value of the beam as a light source is minimal during colliding experiments.

## Slide 19: Extremely Short Bunch
Some experiments (e.g., plasma) may require extremely short bunches
  SLAC FACET delivered ~20mm bunches, FACET-II even shorter
In ILC, if DR is skipped, one can reach such short bunches for electron
  5GeV electron injector  DR  immediately extract from DR  Bunch compressor (see green line below)
  However, as pointed out in [E-1] the present ILC adopts DC gun for polarization. The bunch length is comparable to that in the DR.
  By installing RF gun like at Euro-XFEL in parallel with the polarized gun, the bunch length after the bunch compressor will be 15-30mm bunches
Not a parasitic mode. But presumably possible if one can get hours/day machines time
Beam dynamical issues to be studied
  Coherent radiation in the turn-around and the bunch compressor
  Higher-order mode loss in the main linac
Bunch Compression
Bunch Compression

## Slide 20: Extraction at midway in ML
Extraction other than at the beam dumps is possible only under several conditions
Must estimate the necessary space and device for extraction
  kicker, pulsed magnet
In the beginning there will be several empty places where accelerator modules are absent. They are reserved for the case the accelerating gradient were not sufficient. However, the detail of their location is still under consideration.

## Slide 21: An example: Extraction of 45GeV Beam?
Serious studies are needed for extraction at midaway
It might be possible to adjust the beam energy to 45GeV at ML end by reducing the accelerating gradient once in several pulses.
  To reduce the gradient once in a while is possible (to turn of some acceleration cavities is difficult because quick detuning is needed)
  See next page for detailed consideration
  The figure below is the electron side., but the posistron side is almost the same. The dump near the center of this figure is [E+4] in the positron side.
E-4

## Slide 22: Extraction of 45GeV Beam? (continued)
It is hard to change the strengths of the quadrupole/steering magnets, i.e., orbit retuning is impossible, hence beam quality would be worse
  In the past we made a study whether alternating operation with 45GeV (for Z-pole) and 125GeV is possible or not. In that case the orbit was tuned to 45GeV beam, and the answer was yes though the emittance of 125GeV beam became larger several times. However, the case where the orbit is tuned to 125GeV beam has not been studied yet. Presumably, significantly worse.
Final Focus System contains dipole magnets. The beam must be separated out before these bends.  should lead the beam to [E+4]
  This dumpline is set up to accept 125GeV beam. Can it accept 45GeV beam? Presumably yes, but must take into account of the required optics for the parasitic experiment.

## Slide 23: Caution
Extension of the tunnel
  If built at the first construction, it is not too expensive (compared with the ILC project cost, not the cost of parasitic experiments).
  The major problem of later extension of the tunnel is not the additional cost but the point whether the tunnel construction machine can be brought into the tunnel where the accelerator components are already sitting.